## Slide 1: Stereo Depth Estimation
Ishan Gupta, Asavri Kaur, Vasilis Pteris, Alexandra Ukrainskaya

## Slide 2: Project Outline - SGBM
The Semi-Global Block Matching (SGBM) algorithm was chosen superior level of detail and accuracy in textured environments compared to alternative methods.
Translation of C++ logic into HLS compatible code
Hardware-software targeting FPGA fabric
Optimisation of HLS to target optimal performance

## Slide 3: Specific Aims
Throughput
Potential scope to achieve real time depth estimation of 161 ±10% FPS at 1080p resolution, to meet deterministic timing requirements of high-speed optical systems.
Resource Utilisation
Optimise resource efficiency to ensure the design fits below a utilisation maximum threshold of 70% for BRAM, DSP, LUT and FF.
Speedup Validation
Quantify a speed up of 10x times the benchmarked software runtime to demonstrate the efficiency of custom hardware accelerated cost aggregation paths.
https://www.xilinx.com/support/documents/sw_manuals/xilinx2022_2/ug949-vivado-design-methodology.pdf
FP-Stereo: Hardware-Efficient Stereo Vision for Embedded Applications | IEEE Conference Publication | IEEE Xplore
Disparity Map Validation
Verify correctness of the output disparity maps against benchmarked C++ code and known test images.

## Slide 4: Algorithm to be accelerated – Asavri/Ishan
PROGRAM StereoDepth
left, right ← load stereo pair
fx, baseline, doffs ← load calibration
resize images to 25%
disparity ← SGBM(left, right) // pixel shift per point
FOR each pixel:
IF disparity > 0:
depth ← baseline × fx / (disparity + doffs) // mm
save disparity map, depth map, raw depth
END
Left image
Right image
Software Implementation
--- Timing (741x500, maxDisp=80) ---
load images: 300.679 ms
resize + save: 19.3048 ms
SGBM (cold): 35.8756 ms
SGBM best of 10: 28.8824 ms (12.8279 Mpix/s)
depth conversion: 2.4578 ms
visualize + save: 262.639 ms
Disparity map
Depth map

## Slide 5: Investigation so far - Alexandra
SGM has offers great speed/accuracy trade-off among local/global/semi-global stereo matching algorithms[1]
General stereo depth camera pipeline is capture → calibrate → rectify → stereo matching (SGM) → disparity-to-depth triangulation [2]. The pipeline for stereo matching (SGM), which we are going to accelerate, is cost →aggregation → disparity → refinement[3].
Existing FPGA solutions: Vitis Vision Library[5] has PL implementation of functions that may be used for stereo vision; FP-stereo open-source library for stereo camera pipelines[5].
Global optimization causes heavy memory pressure on hardware (large intermediate results, irregular access) → cost aggregation is the FPGA bottleneck [6]
[1]H. Hirschmuller, "Stereo Vision in Structured Environments by Consistent Semi-Global Matching," 2006 IEEE Computer Society Conference on Computer Vision and Pattern Recognition (CVPR'06), New York, NY, USA, 2006, pp. 2386-2393, doi: 10.1109/CVPR.2006.294.
[2] R. Szeliski, Computer Vision: Algorithms and Applications, 2nd ed. Cham, Switzerland: Springer, 2022, ch. 11-12.
[3] R. A. Hamzah and H. Ibrahim, "Literature survey on stereo vision disparity map algorithms," Journal of Sensors, vol. 2016, Art. no. 8742920, 2016, doi: 10.1155/2016/8742920.
[4] AMD, "Stereo Vision Pipeline," Vitis Vision Library, version 2023.2, Dec. 2023. [Online]. Available: https://docs.amd.com/r/2023.2-English/Vitis_Libraries/vision/overview.html_3_5.
[5] J. Zhao, T. Liang, L. Feng, W. Ding, S. Sinha, W. Zhang, and S. Shen, "FP-Stereo: Hardware-efficient stereo vision for embedded applications," in Proc. 30th Int. Conf. Field-Programmable Logic and Applications (FPL), 2020.
[6] W. Wang, J. Yan, N. Xu, Y. Wang, and F.-H. Hsu, "Real-time high-quality stereo vision system in FPGA," in Proc. Int. Conf. Field-Programmable Technology (FPT), Kyoto, Japan, 2013, pp. 358–361, doi: 10.1109/FPT.2013.6718387.

## Slide 6: Project Plan (Milestones & Timeline)
Benchmarking PS (Completed end of week 5)
Implementing on PL (Complete end of week 7)
Optimizing PL (Complete end of week 8)
Peripheral Integration (Stereo Cameras) [Complete end of week 8/ongoing into week 9]
Report (Ongoing, due week 10)

## Slide 7: Risks and Contingencies - Asavri
Risk | Likelihood | Impact | Mitigation
SGM cost aggregation exceeds on-chip memory (BRAM) | H | H | Reduce disparity range/resolution (quality validated in SW at 0.25×); 4 aggregation paths instead of 8; fall back to local BM (xf::cv::StereoBM)
HLS kernel misses timing / throughput target | M | M | Lower clock or parallelism; use proven Vitis Vision SemiGlobalBM IP as baseline, custom kernel as stretch
No physical stereo camera | M | L | Full pipeline runs on Middlebury dataset pairs
Integration overrun (tool/board issues, schedule) | M | H | Staged deliverables. Each stage is independent. SW -> HLS -> on board -> live camera integration
H = High, M = Medium, L = Low
xilinx.github.io/Vitis_Libraries/vision/2022.1/index.html
2014 Stereo Datasets OpenCV: cv::StereoSGBM Class Reference

## Slide 8: Team Roles
Ishan Gupta – Set up platform, Test on board, Replace with real kernel, Clock tuning and pipeline optimisation.
Asavri Kaur – ARM program, ARM verification, Kernel timing, Pixels-per-clock optimisation testing.
Vasilis Pteris – Kernel in csim, circuit verification, SGM in KV260 and Unroll + Partition sweep testing.
Alexandra Ukrainskaya – Build depth map verification tool, Write printable C++ algorithm, Board output verification, Different data type sizes optimisation testing.